## Slide 1
Web:www.smartagritechs.com Email:muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Real Time Weed Detection using Deep Learning

## Slide 2
Web: www.smartagritechs.com Email: muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Problem Statement
Weed and crop compete for nutrients, water and land.
Reduced production of required crop.
Correct weed identification important for effective weed control.
Pesticide application needs to be effective.
Lower amount of pesticide required.
Shield crops from pesticide application.
Cirsium Arvense weed of wheat crop

## Slide 3
Web: www.smartagritechs.com Email: muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Solution 1/2
Multi-class weed detection using deep learning techniques
On field deployment using Embedded-AI to achieve practical results

## Slide 4
Web: www.smartagritechs.com Email: muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Solution 2/2
Real time detection for targeting weeds using deep neural networks.
Weeds targeted are of different types and at different stages of growth.
Robust solution for quick deployment and portability.

## Slide 5
Web: www.smartagritechs.com Email: muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Layout
Nvidia Jetson Nano
(mobile device)
Deep Neural Network
Custom Dataset
USB Webcam
Training
Deployment
Real time detection
Optimizations
Increase FPS
Reduce inference time
Improve real time accuracy
Data Preparation
Image Sourcing
Labelling
Image Augmentation

## Slide 6
Web: www.smartagritechs.com Email: muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Deep Learning Workflow
INFERENCE

## Slide 7
Web: www.smartagritechs.com Email: muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Software Used
Frameworks
  Darknet
  ONNX
  Tensorflow
Optimization Libraries
  TensorRT
  CUDA
  OpenCV
Implemented using Python

## Slide 8
Web: www.smartagritechs.com Email: muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Model Architecture
Model used
  Yolov4-tiny (Darknet)
    Lightweight and accurate
    Suitable for edge devices with low computing capacity and power
Model Configuration
Classes = 2
Image Input Size = 416 X 416 X 3
Momentum = 0.9
Decay = 0.0005
Learning rate = 0.00261

## Slide 9
Web: www.smartagritechs.com Email: muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Network Structure
18
18

## Slide 10
Web: www.smartagritechs.com Email: muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Procedure

## Slide 11
Web: www.smartagritechs.com Email: muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Image Sourcing 1/2
  Two types of weed are taken into consideration for this project:
    Cirsium Arvense (Wheat Crop Weed)
    Groundnut Weed
  Images for training the model were sourced from local fields.
  Number of viable Images obtained were as follows:
    Cirsium Arvense: 221 images
    Groundnut Weed: 267 images

## Slide 12
Web: www.smartagritechs.com Email: muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Image Sourcing 2/2
  Example images for Cirsium Arvense
  Example Images for Groundnut Weed

## Slide 13
Web: www.smartagritechs.com Email: muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Image Augmentation 1/2
  Number of images increased through combination of various augmentation techniques:
    Translational: Rotation, Flipping, Random Cropping
    Colour Adjustments: Brightness, Contrast, Blur
  Number of images after augmentation:
    Cirsium Arvense: 1607 images
    Groundnut Weed: 3780 images
  Total images: 5387.

## Slide 14
Web: www.smartagritechs.com Email: muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Example Modifications
+20% Contrast
+20% Brightness and Blur
Rotate 90ᴼ clockwise
Flip Horizontally

## Slide 15
Web: www.smartagritechs.com Email: muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Augmentation Significance
  Artificially increase number of images:
    Translated images are considered new images by the model.
    Better generalization.
  Mimic real time fluctuations:
    Blur mimics dusty camera lens.
    Brightness and Contrast Mimic different possible sunlight conditions.

## Slide 16
Web: www.smartagritechs.com Email: muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Training Pipeline
  The images were labelled using open-source LabelImg tool.
  Yolo format .txt label files were obtained.
  The images, along with label files, were fed to the Yolov4 Tiny model.
  Input Image size: 416 x 416 x 3.
  Training/Test split was 90/10.
  Transfer learning: 29 pretrained convolutional layers (on COCO dataset) used as starting point.
  Training executed on Tesla T4 GPU (Google Colab).

## Slide 17
Web: www.smartagritechs.com Email: muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Deployment
  Deployment mobile device: Nvidia Jetson Nano (4GB).
  Live capture source: A4Tech USB Camera.
  Objective: Optimize real-time interference on mobile device.
    Yolov4 Tiny, though lightweight, operates at 15 FPS average.
    TensorRT engine used at inference time, optimizes model specifically for hardware.
    Model converted from Darknet to ONNX to TensorFlow/TensorRT.
    TensorRT-Float16 optimization yields 28 FPS average.
    Average detection time: 0.12 ms.

## Slide 18
Web: www.smartagritechs.com Email: muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Benchmarks 1/2
  Training benchmarks @ confidence threshold 0.25
    Class-wise mAP:
      Cirsium Arvense: 94.81 %
      Groundnut Weed: 88.44%
mAP | Precision | Recall | F1 Score
91.63% | 0.80 | 0.89 | 0.84
Unique Truths | True Positives | False Positives | False Negatives | Mean IoU
2533 | 2248 | 574 | 285 | 64.14%

## Slide 19
Web: www.smartagritechs.com Email: muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Benchmarks 2/2
  Inference benchmarks on Nvidia Maxwell GPU with 128 CUDA Cores (Jetson Nano GPU)
Average Detection time | GFLOPS | Average FPS | Optimized Average FPS
5.02 ms | 6.789 | 15 | 28

## Slide 20
Web:www.smartagritechs.com Email:muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Predictions

## Slide 21
Web:www.smartagritechs.com Email:muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Cirsium Arvense

## Slide 22
Web:www.smartagritechs.com Email:muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab

## Slide 23
Web:www.smartagritechs.com Email:muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab

## Slide 24
Web:www.smartagritechs.com Email:muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab

## Slide 25
Web:www.smartagritechs.com Email:muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab

## Slide 26
Web:www.smartagritechs.com Email:muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Groundnut Weed

## Slide 27
Web:www.smartagritechs.com Email:muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab

## Slide 28
Web:www.smartagritechs.com Email:muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab

## Slide 29
Web:www.smartagritechs.com Email:muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab

## Slide 30
Web:www.smartagritechs.com Email:muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab

## Slide 31
Web: www.smartagritechs.com Email: muhammad.shahzad@seecs.edu.pk
Adaptive Signal Processing Lab
Conclusion and Remarks
  Successful weed detection with decent mAP (90%+) and FPS (25+) benchmarks.
  Shortcomings:
    May not detect all instances in real time.
    FPS still relatively low due to hardware constraints.
  Future Optimizations:
    Train on more images to generalize better.
    Use a mobile device with better performance (costly).